ARM Microcontroller Workshop

---
ARM Microcontroller Workshop

---
What is ARM
- ARM does not sell chips
- ARM sells IP cores
  - See http://en.wikipedia.org/wiki/Semiconductor_intellectual_property_core

---
ARMx vs ARMvx
- ARMx: Family of similar cores.
  - ARM7: since 1998 (ARM7TDMI)
  - ARM11: since 2002 (Raspberry Pi)
  - CORTEX-{A,R,M}
- ARMvx: Version of the instruction set
  - ARMv6: Raspberry Pi v1, ARM7TDMI
  - ARMv7-M: Microcontroller
  - ARMv7-A: Smartphone, Raspberry Pi v2
  - ARMv8-A: Server, future Smartphone (64 bit)

---
CORTEX-{A,R,M}
- Latest architecture from ARM
  - A: Application
  - R: Real-Time
  - M: Microcontroller
    - M0
    - M0+: Improved M0, the smallest core from ARM
    - M1: For FPGAs
    - M3: r0ket
    - M4: latest midrange, with floating point
    - M7

---
Thumb (2) vs. 32 bit ARM
- Traditional ARM instructions are 32 bit long
- Thumb mode was introduced to generate smaller code with 16 bit instructions
  - Thumb2 can use use 16 bit and 32 bit instructions at the same time
- All Cortex-Mx controllers use the thumb mode to execute code.

---
ARM Microcontrollers
- The ARM core is only a small part of an ARM microcontroller
- There are lots of different ways to implement the different peripherals
  - Timers
  - GPIOs
  - DMA
  - USB
  - Ethernet
  - NVIC
- Manufacturers usually supply lots of libraries for these components

---
ARM Microcontrollers

---
Memory Maps
- ARM presents itself as a von Neumann architecture
  - Code, data and peripherals live in the same address space
- To understand whats happening inside the MCU, you should know this memory map

---
Memory Maps

---
Interrupts
- Interrupts can be caused by hardware components
  - They interrupt normal code execution and cause a jump to another code region
  - Reset is also an interrupt!
- The MCU needs to know where to jump to
- The vector table contains a list of addresses
  - Each entry corresponds to an interrupt source
- After reset, the table is expected at the start of the flash memory
- Initial stack pointer value is the first entry

---
Interrupts

---
Memory Mapped I/O and Peripherals
- All interaction with the GPIOs and other peripherals goes through memory mapped I/O
- There are no special I/O instructions
- Consult the datasheet for memory addresses of the different peripherals

---
Toolchains
- Keil MDK-ARM
- IAR Embedded Workbench
- ARM Development Studio
- gcc
  - Focus of this workshop
  - Patches maintained by ARM
  - https://launchpad.net/gcc-arm-embedded

---
Setting up gcc for ARM
1. Grab the archive for your system from https://launchpad.net/gcc-arm-embedded/+download
2. Extract archive
3. Add gcc-arm-none-eabi-4_9-2014q4/bin to you PATH
4. Verify by calling arm-none-eabi-gcc -v

---
Setting up Chip tools
- Grab stlink from https://github.com/texane/stlink
- Build
- Install udev rules (or run tools with sudo)
- st-util acts as a gdbserver to allow debugging and flashing
- See: http://www.wolinlabs.com/blog/linux.stm32.discovery.gcc.html

---
Contents of the project template
- Makefile
  - Build instructions for the project
- Linker script
  - Defines Memory layout and sections
- Device specific headers and libraries
  - Describe peripherals and chip properties
  - CMSIS + STM32 drivers

---
- Get datasheet, reference manual, programmers guide and errata
- Hello world (blink an LED)
- Compile
- Flash
- Profit