ARM Microcontroller Workshop

---
ARM Microcontroller Workshop

---
What is ARM
- ARM does not sell chips
- ARM sells IP cores
  - See http://en.wikipedia.org/wiki/Semiconductor_intellectual_property_core

---
ARMx vs ARMvx
- ARMx: Family of similar cores.
  - ARM7: since 1998
  - ARM11: since 2002 (Raspberry Pi)
  - CORTEX-{A,R,M}
- ARMvx: Version of the instruction set
  - ARMv6: Raspberry Pi
  - ARMv7-M: Microcontroller
  - ARMv7-A: Smartphone
  - ARMv8-A: Server, future Smartphone (64 bit)

---
CORTEX-{A,R,M}
- Latest architecture from ARM
  - A: Application
  - R: Real-Time
  - M: Microcontroller
    - M0
    - M0+: Improved M0, the smallest core from ARM
    - M1
    - M3: r0ket
    - M4: latest midrange, with floating point
    - M7

---
Thumb (2) vs. 32 bit ARM
- Traditional ARM instructions are 32 bit long
- Thumb mode was introduced to generate smaller code with 16 bit instructions
- All Cortex-Mx controllers use the thumb mode to execute code.

---
ARM Microcontrollers
- The ARM core is only a small part of an ARM microcontroller
- There are lots of different ways to implement the different peripherals
  - Timers
  - GPIOs
  - DMA
  - USB
  - Ethernet
- Manufacturers usually supply lots of libraries for these components

---
ARM Microcontrollers

---
Memory Maps
- ARM presents itself as a von Neumann architecture
  - Code, data and peripherals live in the same address space
- To understand whats happening inside the MCU, you should know how this memory map

---
Memory Maps

---
Interrupts
- Interrupts can be caused by hardware components
  - They interrupt normal code execution and cause a jump to another code region
- The MCU needs to know where to jump to
- The vector table contains a list of addresses
  - Each entry corresponds to an interrupt source
- After reset, the table is expected at the start of the flash memory
- Initial stack pointer value is the first entry

---
Interrupts

---
Memory Mapped I/O and Peripherals
- All interaction with the GPIOs and other peripherals goes through memory mapped I/O
- There are no special I/O instructions
- Consult the datasheet for memory addresses of the different peripherals

---
- What is ARM?
- ARMx vs ARMvx
- CORTEX-{A,R,M}
- Thumb(2) vs 32bit ARM instruction set
- Differences between different ARM MCUs
- Memory Map
  - ISR Vector Table + Stack
- Register/Ports (vs I/O instructions)

---
- Toolchains: gcc, iar, rvds, cmsis(?)
  - Install Arm toolchain from launchpad
- Linkerscripts
  - From our repo
- Startup code
- Makefile
  - compiler
  - linker
  - Size
  - Objcopy

---
- Get datasheet, reference manual, programmers guide and errata
- Hello world (blink an LED)
- Compile
- Install St-link
  - http://www.wolinlabs.com/blog/linux.stm32.discovery.gcc.html
- Flash
- Profit